Practical Applications

# sim_basic: Simulation

This lab aims to refresh your knowledge of Verilog basics and simulator usage.
Hint! You should use some of the following constructs:
- preprocessing: `include, `define
- tasks, functions, variable declarations
- module/interface, instantiation
- event control: @(…), #x ns
- loops: repeat, for, forever
- assignments: continuous (assign), blocking (=), non-blocking(<=)
- randomization: $urandom, std::randomize(x)
- string formating & printing: $sformatf, $display
All these can be found in the Verilog quick reference card.
## Clock and Reset
1. Define the ex_clk_rst_gen module with 2 outputs:
  clk is the generated clock signal
  rst_n is the negative logic reset signal (i.e. active low)
2. Define the CLOCK_PERIOD parameter which determines the clock period
3. Implement a clock generator
4. Implement an initialization block for the reset&clock signals
5. Implement a task drive_reset() that drives the reset signal for 3cc
## Interface
declare an interface ex_out_if that has 2 ports:
- input logic clk
- input logic rst_n
declare inside ex_out_if 2 signals:
- data : 8 bits, of type logic
- valid : 1 bit, of type logic
implement a task drive_data inside ex_out_if that:
- drives 5 random data on the bus, with [1..5] cc in between
- each data is driven on posedge of the clock
- when valid signal is asserted it indicates the data is valid
- for each of the 5 data the task prints its value
- after it finishes to send data, it waits for 3 cc and stops the simulation
  - Hint: Use $stop()
Declare an interface ex_in_if that has 2 ports:
- input logic clk
- input logic rst_n
Declare inside ex_in_if two signals:
- data : 8 bits, of type logic
- valid : 1 bit, of type logic
Implement a function format_data that
- has one byte argument
- creates a string that prints the byte in hexadecimal format (e.g. "Data is 0xAB")
- returns the string
implement a task monitor_data inside ex_in_if that:
- It monitors continuously the data and valid signals
- it samples the data/valid signals on the posedge of the clock
- when valid signal is asserted it indicates the data is valid
- prints the data on the screen using the format_data function
## Top module
1. declare reset and clock signals using wire
2. instantiate ex_clk_rst_gen and connect it to the clk and reset wires
3. declare the data(8bit) and valid(1bit) wires
4. instantiate ex_in_if and:
- connect it's ports
- connect it's internal signals to data and valid wire
instantiate ex_out_if and:
- connect it's ports
- connect it's internal signals to data and valid wires
In the initial block you should:
- drive reset 4 times by calling the reset task defined in the ex_clk_rst_gen
- start the ex_out_if.drive_data and ex_in_if.monitor_data tasks to run in parallel.
- once they finish call the $stop system task.
## Time to simulate
Using the simulation scripts from ${PROJ_HOME}/sim, compile and start the simulation. You will need to add each signal that you want to observe to the waveform.

# sv_basic: SystemVerilog Basics
## Set up your file structure
Copy ex_clk_rst_gen.v, ex_intf.sv, ex_top.sv from the previous part to sv_basic/tb folder
## Enumerations
1. Open ex_scratch.sv.
2. Define an unsized enumeration color_t that has the following items: RED, GREEN, BLUE, YELLOW, BROWN, ORANGE
3. Define a sized enumeration error_t on 2 bits that has the following items: FVC_NONE, FVC_INFO, FVC_WARNING, FVC_ERROR
## Classes
Declare a class "first_class"
- add 4 fields of type : color_t, byte, unsigned integer, 32x5-bit array
- implement its constructor and initialize each element in the array to be equal to its index
- implement a function get_string() which returns a string similar to "My fields are: color=RED, byte=0x23, uint=14524535, array=[0x00, 0x1F, .…]"
- implement a function print_me() that displays the string returned by get_string()
- Implement a function compute_crc() that computes an 8bit crc by XOR-ing individual elements
Declare a class "second_class" that inherits "first_class"
- declare an error_t field
- implement a constructor that calls the first_class constructor and then sets the error_t field to be INFO
- override the get_string() method to also include the error_t field
Declare a class called "run_container"
- declare a field of type first_class
- declare a field of type second_class
- initialize the two fields in the constructor
## Constraints and Randomization
1. declare the color_t, byte and the array fields of first_class as randomize-able
2. In the run_container play with the randomization: generate 100 items and print them.
3. Play with the following types of constraints:
- constant value
- values within a range
- values outside of a range
- conditional constraints
- iterating constraints
- order constraints
## Exercise: Tree
1. Implement a tree structure using SystemVerilog. Each node has the following fields:
  1. color (you can use color_t from previous examples)
  2. sibling index: indicates the node index inside the list of siblings
  3. depth: indicates the depth of the node (0-root node)
2. The tree should have a depth of maximum 8 and each non-leaf node can have at most 4 children. Once the tree structure is defined you should initialize&display trees for the following cases:
  - depth = 5, only 2 child nodes / parent
  - depth = 3, random number of child nodes
Each node should implement a
  - print_me() method that displays the current node
  - print_tree() method that displays recursively, top-bottom, the whole tree
# sv_basic: SystemVerilog Basics
This lab aims at introducing the “fork” statement and the concept of driving and monitoring using tasks and functions. Starting from the provided code:
## master_driver:
  - Write a task for driving data. Task should have the following argument: addr, wnr, wdata.
  - Write a task that randomizes and drives addr, wnr, wdata. If a read operation is desired, wdata must be 0.
  - Write a function that prints to the console all information regarding a transfer. Call this function at the end of a transfer to print all its data.
  - Driving task should also take reset into account.
## slave_driver:
  - Write a task for receiving a transfer and returning random rdata if needed. Busy must also be driven by the slave_driver and be randomized to last between 0 and 30 clock cycles.
  - Write a function for printing a received transfer. Call it at the end of each transfer.
  - Driving/receiving task should also take reset into account.
## tb:
  - Inside a fork statement drive both the 2 masters and the slave and observe packets printed by masters and slave. By calling the drive functions from masters and slave create scenarios in order to test that the DUT (demux2:1) performs as intended. Note that the demux gives higher priority to master0 than master1.
Protocol used must obey the following rules:
- cmd signals the the master wants to initiate a transfer
- busy indicates whether the slave can or cannot accept the transfer
- a valid transfer takes place when cmd is high, busy is low, and all signals are not unknown
- An example of a valid write and read is shown below. For both transfers the DUT stalls the transfer for 1 clock cycle by asserting busy. The first transfer is a write, signaled by wnr high, while the second transfer is a read, wnr is low.